## Slide 1: INTRODUCTION TO GEARS & GEAR RATIOS
Brought to you by:
Electric Vehicle Challenge

## Slide 2: WHAT IS A GEAR?
A gear is a wheel usually made of metal or plastic with teeth that meshes together with other gears to transfer rotational energy
Watch/
Clock
Drill
Bicycle
Wind-up
Toys
Vehicle Transmission

## Slide 3: DIFFERENT TYPES OF GEARS
Spur Gears
Bevel Gears
Worm Gears
Pulley Gears

## Slide 4: GEAR RATIOS
What is a Ratio?
  The number of times one number can be found within another.
  Example: There are three 2’s in six [6/2 =3]
What is a Gear Ratio?
  A Gear Ratio is the number of times a gear will turn in full when compared to another gear
2
1
:

## Slide 5: FINDING GEAR RATIOS TWO GEARS
Driver Gear
Driven Gear

## Slide 6: FINDING GEAR RATIOS COUNT THE TEETH ON EACH GEAR
Driver Gear
Driver Gear
Driven Gear
Driven Gear

## Slide 7: FINDING GEAR RATIOS DIVIDE ONE TEETH COUNT BY THE OTHER
Driven Gear
Driver Gear

## Slide 8: LET’S GIVE IT A TRY! WHAT ARE THE RATIOS OF THESE GEAR COMBINATIONS?
40 teeth
40 teeth
20 teeth
1
2
100 teeth
25 teeth
3
1
1
/
/
2
1
/
4
1
40 teeth
Driven Gear
Driver Gear
Driver Gear
Driver Gear
Driven Gear
Driven Gear

## Slide 9: TORQUE VS. SPEED
What is torque?
Torque is a measure of the force needed to get an object to rotate
What is speed ?
Speed is how fast your gears are spinning.
*Rotations per Minute (RPM)
Torque and speed are relative to one another when comparing them with the output power of the motor.
POWER = Torque * Speed

## Slide 10: TORQUE VS. SPEED (CONT.)
What happens when you change the speed or the torque?
Power Output
(1150 W)
=
*
Torque
(5.5 N-m)
Speed
(2000 RPM)
POWER = Torque * Speed

## Slide 11
Stall Torque
12.7 N-m for our motor
No Load Speed
5,200 rpm for our motor
Rotational Speed
Torque
Max Power

## Slide 12: LET’S GIVE IT A TRY! WHICH ONE OF THESE WILL GIVE YOU MORE TORQUE AND WHICH ONE WILL GIVE YOU MORE SPEED?
Torque
Speed

## Slide 13: GEAR RATIO LAB SETUP
50-tooth gear
40-tooth gear
40-tooth gear
20-tooth gear
10-tooth gear